## Slide 1: Francisco Barranco Cornelia Fermüller Yiannis Aloimonos
Event-based contour motion estimation

## Slide 2
Asynchronous Event-based Dynamic Visual Sensor
[1] P. Lichtsteiner, C. Posch, and T. Delbruck, A 128×128 120dB 15μs latency asynchronous temporal contrast vision sensor, IEEE J. Solid State Circuits, 43(2), 566–576, 2008.
[1]
No blurring, no artifacts
Accurate fast motion estimation
No occlusions
Real-time performance
DVS output  asynchronous AER
At point P(u,v), at time t an event event(u,v,t) of value either +1 or -1 is fired if the logarithm is greater than T
DAVIS/ApsDVS or ATIS:
Dynamic + static scene information
Provide absolute scene-reflectance values

## Slide 3
Motion pathway with Dynamic Visual Sensor
Early contour boundaries
Rough motion estimation
Early segmentation
Refined motion estimation
3D pose estimation
- Accurate motion estimation
No additional assumptions
Only estimates in the contours
High temporal resolution

## Slide 4
Problems of current approaches | DVS Camera solution
Handle fast motion Solution: Multiresolution techniques 3D motion from matching interest points not from motion | High temporal resolution
Depth discontinuities | Early extraction of contours
Separate different 3D motions | The high temporal information allows separating two different rigid motions superimposed
Computational cost | Compute normal flow only when there is a change in time
Motion blur, light artifacts | Dynamic range (log)
Event-based contour motion estimation

## Slide 5
Contour motion estimation
Speed local bar width
With:
 #events of pixel p
 Set of connected pixels
 speed for pixel p
Robust function for the sign estimation
Figure. Events collected with the DVS camera zooming in a chessboard pattern. The first row show the collected positive (black) and negative (red) events for the row 70, and an example of the output of the DVS.
Fusing DVS and Intensity data:
Accurate intensity reconstruction for every event

## Slide 6
Contour motion estimation
Figure. Events collected for “Translation Tree” sequence The first row shows the image and the accumulated positive events. The second and third row show the positive events collected for row 80 of the image. The last row shows the speed estimated for pixel (80, 40) for different time intervals (over 3300ms at a step size of 100ms).
Speed local bar width
+ multi-temporal approach
Early segmentation
Refined motion estimation

## Slide 7
Problem I: Fast speed estimation
Video source: http://www.youtube.com/watch?v=arlWwQsmnM
Handle fast motion multiresolution techniques
Time performance
Computational complexity
Not very accurate:
- Scale-to-scale error propagation
- Outliers suppression
Small objects moving fast
[2] D. Sun, S. Roth, and M. Black, A quantitative analysis of current practices in optical flow estimation and the principles behind them, IJCV, 106 (2), 115–137, 2014
Solution: High temporal resolution (DVS)
classic+NL-fast

## Slide 8
Problem II: Occlusions
Detect and prevent:
- Reprojection
- Flow divergence
Flow available  ++ Error
Solution: with DVS occlusions do not make sense
 | AEPE rel (%) | AEPE rel (%) [2] | Density (%)
Classic+NL-fast [2] | 0.619 | 26.1 | 4.165
Event-based | 0.261 | 9.6 | 4.165
[3] B. McCane, K. Novins, D. Crannitch, and B. Galvin, On benchmarking optical flow, Computer Vision and Image Understanding, 84 (1), 126 – 143, 2001.
Figure. Satellite sequence [3]. Occlusion results for event-based and Classic+NL-fast[2] algortithm.
Occluded regions + smoothing constraint 
Error propagation

## Slide 9
Problem III: Performance
 | Frame rate | Frame rate [2] | Events
Satellite 200x200 | 31.6 fps | 0.07 fps | ~15000
Real-time performance with DVS
Conventional sophisticated methods:
Texture decomposition
Multiresolution schemes
Nonconvexity weighing functions
Spline-based bicubic interpolation
Global smoothing terms
Non-local regularization terms
Actual framework seems to be exahusted
- Without an early motion boundary segmentation obtaining more accurate methods is very hard
Computationally very expensive
It might take even minutes
 | AEPE rel (%) | AEPE rel (%) [2] | Density (%)
Trans | 0.003 | 7.5 | 9.72
Diver | 15.4 | 19.4 | 5.4
Yosemite | 12.8 | 11.7 | 1.37
Rubberwhale | 25.2 | 40.1 | 0.53
Dimetrodon | 7.2 | 9.1 | 0.78
Satellite | 9.6 | 26.1 | 4.17
Our contour motion estimation is more accurate than [2], algorithm ranked in Middlebury [4] as one of the first ones in December 2013!!

## Slide 10
 | AEPE rel (%) | AEPE rel (%) [2] | Density (%)
Trans | 0.003 | 7.5 | 9.72
Diver | 15.4 | 19.4 | 5.4
Yosemite | 12.8 | 11.7 | 1.37
Rubberwhale | 25.2 | 40.1 | 0.53
Dimetrodon | 7.2 | 9.1 | 0.78
Satellite | 9.6 | 26.1 | 4.17
[4] S. Baker, D. Scharstein, J. P. Lewis, S. Roth, M. J. Black, and R. Szeliski, A database and evaluation methodology for optical flow, Int. J.
Comput. Vision, 92 (1), 1 – 31, 2011
Event-based contour motion results
Our contour motion estimation is more accurate than [2], algorithm ranked in Middlebury [4] as one of the first ones in December 2013!!

## Slide 11
Current framework seems exahusted  DVS
  Asynchronous event-based data
  Multi-temporal biologically inspired approach
  Accurate motion estimation
  Real-time performance / less resources
  No occlusions
Fusion with current frame-based technique
Take-home message