## Slide 1: DWImager SOFTWARE
Quick tutorial
By Poliana Toledo (2021) PhD candidate, co-tutelle Campinas and Granada Universities

## Slide 2: Opening EPMA X-ray maps
Create an archive folder anywhere you want in your pc.
Copy and rename the EPMA X-ray .txt files, giving each file the correspondent element name.
Open the DWImager executable file (2 clicks).

## Slide 3: Opening EPMA X-ray maps
You can open the .txt files by dragging them into the program window or using in the File>Open command.

## Slide 4: Opening EPMA X-ray maps
Press File>Save All to save the images in .img extension.
To view all images in the screen, press Window>Tile Vertically or Tile Horizontally.
Go to View>Smooth to smooth the pixelated aspect of the images.

## Slide 5: Opening EPMA X-ray maps
Double click in the Mg image and check the information shown.
The Label/Notes tab must show the element name and the X-ray line in Image Label.
In the Registration tab, click in Z registration to check coordinates of the image center and vertices.

## Slide 6: Opening EPMA X-ray maps
In the EPMA tab check if the Element name and X-ray line are correct. It can be unwritten for elements that are abbreviated with only one letter (e.g., K, S, P, F) so you must insert the information and click in apply, then close.
Close the images that are not useful to identify minerals (especially the acquired by EDS), either because the signal is very low (ex: As, Cu, Ce) or because they are showing interference with other elements (e.g., F and Fe, Zr and P, Y and P).

## Slide 7: Observing elements distribution
Open the Mn image and expand the color bar located in the bottom of the window by dragging its upper limit above. You will see the garnet pixels shown in the color bar in the range of green to yellow colors.
You can change and custom the color palette as you wish, by clicking in the Palette menu, or in the icons

## Slide 8: Observing elements distribution
To enhance garnet Mn zoning, drag the left and right bars of the color bar and limit the range to show only garnet pixels.
As default, pixel intensities above the selected values are shown in red. You can change it by clicking in View>Background, and red pixels will become invisible.

## Slide 9: Observing elements distribution
You can also change the pixels intensities scale for log scale clicking in Log, and then Lin to go back to the linear scale.
Zoom in to view details of the image clicking in the arrow next to the Fit to window button and selecting a number or writing the percentage of zoom.
Now click in Image>Adjust to ROI, or in the icon The image is now showing all the pixels once again.

## Slide 10: Observing elements distribution
Click in Image>Set ROI or in the icon
Draw a rectangle in the image biotite-rich matrix, as shown in the figure.
Click again in the Set ROI icon and then in the Adjust ROI icon. Color scale is now adjusted to evidence Mn intensities and variations for the selected area and pixels in the same count range.

## Slide 11: Observing elements distribution
If you want to evidence the counts range of the same area in other maps, you can simply click on Image>Transfer Properties, select the Image ROI and palette option and select the elements you want in the Transfer to: window.*
Go to the maps of elements you selected and click in the Adjust to ROI icon. Click again in the Set ROI then the Adjust ROI icons and the image will show all counts range again.
*You can also transfer other properties with this tool, as background configuration and mask (explained in the next steps), EPMA information and objects.

## Slide 12: Observing elements distribution
You can create copies of any images if you want. Just click in Image>Clone and then save the copied image.
In the Object menu, you can insert color and dimension scales, label and objects in the images as you want.
Export this image by clicking in File>Save as and choosing .bmp or .tiff file type.
dimension scale
object
label
color scale

## Slide 13: Observing elements distribution
Use the Image Math icon to generate images with calculations
Select all elements in Sel All to be able to use all for calculations
Choose a name for the calculated image in Math image name
Write the expression and press create
In this example, the number of Fe (#Fe) is calculated, but many calculations are possible.
All the available operators and functions are shown in the Image Math window.

## Slide 14: Observing elements distribution
Check the properties of the generated image.
Rename the map in Image Label and press apply

## Slide 15: Making binary and ternary diagrams
You can inspect elements distributions in binary or ternary diagrams.
Go to Tools>Density Plot. In the opened window, select a base image and the components you want to use as axes.
Choose plot type (binary or ternary). You can check the boxes for log values and/or percent if you want.
Rename the new image and click on create.
The generated graphic shows all pixels of your image in respect to their number of counts of each element chosen.

## Slide 16: Making binary and ternary diagrams
Beware that ternary graphs show the proportions between three elements:
For example, in an Al-Fe-Ca ternary, pixels with no Fe and Al counts (0 or near 0) and with any counts of Ca (from 1 to several thousands) will all plot in the Ca vertex, even though they are not necessarily Ca-rich, but really Fe- and Al-poor.
Binary diagrams, on the other hand, represent, quantitatively, the real number of counts per element.
You can use these graphs to select pixels and create mineral masks. This will be explained in the next steps.

## Slide 17: Creating masks
You can create a mask identifying minerals by narrowing the color scale to evidence the pixels contained in the mineral of interest.
For garnet, for example, you can select the pixels contained in the mineral in the Mn, Mg, Ca and Si maps.
Go to Tools>Threshold Mask and select the maps (Mn, Si, Ca, Mg).
In Mask descriptor write Garnet and press create.

## Slide 18: Creating masks
Go to Object>Mask legend to see the percentage of pixels selected in the mask.

## Slide 19: Creating masks
You can repeat this process, using different combinations of elements and creating different masks for garnet and other minerals.
Then you can exclude the masks you don’t want/need to use by right clicking in the mask image window, selecting properties and choosing the mask you want to exclude and then clicking in the X button.
You can also select/unselect masks in the lower part of the right menu.

## Slide 20: Creating masks from diagrams
You can also choose pixels in bynary or ternary diagrams to create a mask
Make a bynary Si vs #Fe density plot using Si as base image
Draw a rectangle containing the pixels of interest
Right click in the diagram and choose Plot Selection Mask
Choose a name for the mask and press create

## Slide 21: Creating masks from diagrams
If you want, you can draw other shapes selecting Add object>Shape and choosing the shape properties

## Slide 22: Creating a background image
Go to Tools>“Z” Image.
Select the Al as base image and than select all major element. Do not select images acquired by EDS detectors, as they can be displaced from the ones acquired by WDS.
Rename the image as you want, and press create.

## Slide 23: Creating a background image
Select the grayscale in Palette>Grays or in the icon
Adjust the color scale bar to evidence contrasting intensities. You can use this image as a background for the masks you are going to create in next steps.

## Slide 24: Creating a background image
Open the Mask_library window
Go to Image>Configure Background or, to the properties window (double click in the mask image).
In the Background tab, choose the Z image as background image, and check the View background case and Apply.
You can always hide and show background with right click in the mask image and click in “Show background”.

## Slide 25: Creating masks
If you want to see only garnet pixels in the element maps, open one element image and click in Image>Configure Mask or double click in the image and go to the Mask tab in the properties window.
Choose the Mask_library file and press Apply.

## Slide 26: Creating masks
You may have successfully selected the main minerals in your sample, but still, many pixels can be left out of the masks during the selection process.
These pixels can be minerals, mixed signs of different minerals on large pixels, or sample defects (holes with no minerals produced by polishing).
You can investigate these pixels in density plots.

## Slide 27: Creating masks
Open any map image (Ca was used in this example) and click in Image>Configure Mask or double click in the image and go to the Mask tab in the properties window.
Choose the Mask_library file and press Apply inverted.

## Slide 28: Creating masks
In Tools>Density Plot choose Binary and make a graph, using the current map (the one you configured the mask) as base image
Check the Filter with mask of the base image option and rename the new image if you want.
Press Create.
Now you can select the pixels you want to attribute to a mask, as explained before.

## Slide 29: Plotting points to plan EPMA point analyses
If you want to plan point analysis in the X-ray maps, you can plot them in the Imager software and export these points to use in the CAMECA EPMA
Open an element map
In the menu, select Object>Point Locations>New
A new point location layer is created with one default point in the center of the image. This point can be deleted latter

## Slide 30: Plotting points to plan EPMA point analyses
Right click in the image in the point you want to analyze
Press Add Point and label the point with the information you want (mineral name, region, element, etc...)
If you want to delete any point, right click in the point and press Remove Point

## Slide 31: Plotting points to plan EPMA point analyses
After plotting points in the map, save the point locations. Always save before changing the map, or the changes will be lost.
Right click any point and press Save Point Locations
Save as .loc file to use in the Imager software and as .uxyz to use in the CAMECA EPMA
To open the created points file in another map, select Object>Point Locations>Load From File