## Slide 1
Cerebellar Spiking Engine: EDLUT simulator
UGR with input from other partners.
Motivation
Simulation of biologically plausible spiking neural structures
Allow the simulation of different neuron models
Allow the incorporation of new neural features into neuron models without needing to modify the simulator code.
Real-time simulation of middle-scale neural networks (thousands of neurons).
Cerebellum model
Cerebellum model. Inputs encoding the movement are sent (upward arrow) through the mossy fibers to the granular layer. These inputs encode the desired and actual position and velocity of each joint along the trajectory and also context-related information. Inputs encoding the error are sent (upper downward arrow) through the inferior olive (IO). Cerebellar outputs are provided by the deep-cerebellar-nuclei cells (DCN) (lower downward arrow). The DCN collects activity from the mossy fibers (excitatory inputs) and the Purkinje cells (inhibitory inputs). The outputs of the DCN are added as corrective torque
Using tables
The precision of the simulation will mainly depend on:
  Table size and access mode (interpolation)
  Table structure (coordinate distribution)
    If neuron behavior exhibits abrupt changes along a specific dimension denser sampling is required.
    It is also possible to use non-uniform coordinate distribution
Each incoming spike causes the conductance of the corresponding synapse (gj) to follow an exponential decay function.
When the membrane potential (Vm) reaches the threshold, the neuron emits a spike.
Synaptic plasticity&architecture
Some implementation details
Uniform treatment of all possible events that could occur in the simulation process
  Heritage of Event class.
  Different event types (Shot an unique spike, propagation, TCP/IP communication, synchronization with other system, save the current simulation status, simulation ending …etc ).
  ProcessEvent method implements the specific treatment of each event.
Implementation in C++ for Linux and Windows (with Cygwin) until now .
Same precompiled look up tables both 32bits and 64 bits architectures.
.
Inferior Olive Neurons [48]
Purkinje Cells [48]
Deep Cerebellar Nuclei Cells [24]
[8]
[8]
[8]
[8]
[8]
[8]
[8]
[8]
[8]
[8]
[8]
[4]
[4]
[4]
[4]
[4]
[4]
[8]
Excitatory connections
Inhibitory connections
Teaching signal
Granule Cells [1500]
Joint related Mossy [120]
Joint related Mossy [120]
4 rand
mossy
4 rand
mossy
4 rand
mossy
[20]
[20]
[20]
[20]
[20]
[20]
[20]
[20]
[20]
[20]
[20]
[20]
Plastic synapses
Parallel fibers
Network topology
teaching signal
. . .
. . .
. . .
Mossy fibers
Population coding
Leakage integrate-
and-fire neurons
trajectory in
joint coordinate
Translation of coordinates into spike trains
IN1(t)
IN2(t)
IN-1(t)
IN(t)
Advantages: Spikes of biological neurons are well localized in time and not very frequent. Thus low number of events (sparse coding).
Disadvantages: We need a mathematical expression (or method) to calculate the value of each state variable after an arbitrary time (the time of the next event).
Euler / Runge-Kutta method
(N+1)-dimensional table for vn
Table 1…, Table N
Table-based event-driven simulator
Before the simulation
During the simulation
Conductance-based synaptic input
Neural parameters: Cm, Eexc, τexc, Einh, τinh, Erest, grest
Neural state variables: Vm, Gexc, Ginh
Dependent on: Vm, Gexc, Ginh, t
4-dimensional table Vm(Vm0,Gexc0,Ginh0,Δt)
Dependent on: Gexc, t
2-dimensional table Gexc(Gexc0,Δt)
Dependent on: Ginh, t
2-dimensional table Ginh(Ginh0,Δt)
Simulator
Synaptic Weights
Input Spikes
Output Spikes
Net Definition:
1.-Neurons
-Numbers
-Types
2.-Connections
-Delays
-Synapses
Neuron Model look up tables
-Vm(Vi,Gi,Ge,t)
-Ge(t),...
-Tf(Vi,Gi,Ge)
Tf end(Vi,Gi,Ge)
Function Approximation
Neuron Model Definitions
-Equations
-Table definitions
WEIGHTS.DAT
NET.CFG
MODEL_N.DAT
TAB2.CFG.C
Long Term Depression (LTD):
Each time a spike from inferior olive arrives:
Long Term Potentiation (LTP):
Each time a spike from granule cell arrives at synapse i:
If the end time is not yet reached
Extract the event with the shortest latency from the spike heap
Update the corresponding neuron state to the current event time
Apply the current event effect
Insert new produced event in the spike heap
0
-1
-2
-3
-4
-5
0
0.2
0.4
0.6
0.8
1
Contribution last IO spike arrival (ms)
Amount of LTD
Learning laws
x*e
-x
sin(x)
2
* e
-x
sin(x)
20
* e
-x